## Slide 1: Pacemakers and Implantable Cardiac Defibrillators: Are they really secure ?
Steal a Device Programmer
  Need for Reverse Engineering, Modifications
  Easy to get root mode
  Problem : difficult to set up
Build your own Device Programmer !
  Total cost : 800 $
Eavesdropping on private Information
  What kind ? => Implanting physician, Diagnosis, Hospital,
Device state, patient name, date of birth, serial N°, etc...
  The future holds some promises : devices more sophisticated
ergo a lot more data to be divulged ?
Sniff Vital Signs
  Get the vital signs that the ICD emits
  Need to have an Eavesdropping setup
Drain energy
  Send multiple radio signals to the ICD (“Are you sleeping ?”)
  => Battery lifetime decrease
  Simple : transmit-only
Turn off therapies
  “Stop detecting fibrillation”
  Problem : change of the device state
Affect patient’s physiology
  Induce fibrillation, flood with drugs
  Problem : patient’s safety at great risk
Attacks
Defense
ICD
Solutions ?
  Authenticate device programmers ?
  Encryption ? Passwords ?
Problems
  Need emergency access !
  Patient’s health : top priority
Prototypes defenses VS some of the attacks
  Idea : defend without using battery
  External parties pays for power
Device Programmer
control
Example of prototype : WISP = RFID + computation
WISPer = WISP + code
1: External party authenticate through WISPer
2: If successful WISPer says to ICD “Ok you can use radio”
3: Then the External party can control the ICD
The patient is notified acoustically during the whole time.
The WISP
The Solution
The Test